Downloading the Handy Logo firmware onto a crashed Handy Board

1) At the downloading station, plug the telephone cord from the serial interface into the crashed Handy Board.

2.) Put Handy Board into “download mode” by turning the Handy Board off and then, while holding the Handy Board’s  STOP button, turning it back on again. When you do this you should see the red and green LEDs near the STOP button briefly turn on and then turn off.

3) Using the mouse at the download station, click on the Download button that you see on the screen. (Do NOT click the “Burn the board” button!!) Then select the file called hblogo.s19 and click on OK.

4) Respond to the “Is the Handy Board ready?” prompt by clicking on OK. The download process should begin. The process takes place in two stages, with progress monitored by two successive task bars.

5) When the download completes, click on OK, and turn the Handy Board off and back on again. You should be back in business!