# Laboratory 1 Notes

# Introduction to MIPS/MARS

Computer = programmable information processing machine.

Major components = CPU, Memory, and Input/Output

CPU:  contains 32 user registers = storage for data within the CPU

$zero			- Contains a value of 0

$t0 - $t9  		- Temporaries

$s0 - $s7  		- Saved

$a0 - $a3		- Arguments

$v0 and $v1 		- Return values

The contents of these registers are used as operands in the program instructions.  Although all these registers are general purpose (can be used to store any kind of data), there are conventions for typical usage, as indicated.

There are also 7 other registers with specific purposes that you will soon learn more about.

- Each register contains a 32-bit value (32-digit binary/base 2 number)

- A byte is an 8-bit unit, a word  is a 4-byte or 32-bit unit.

- We often represent the values in hexadecimal (base 16), to be concise

$zero always contains a value of 0, which is stored in 32 bits:

0000 0000     0000 0000      0000 0000      0000 00002 ,  is equivalent to

0 0                    0 0                     0 0                     0  016

Groups of 4 binary digits can easily be converted to hexadecimal:

Decimal	Binary	Hexadecimal

0		0000		0

1		0001		1

2		0010		2

3		0011		3

4		0100		4

5		0101		5

6		0110		6

7		0111		7

8		1000		8

9		1001		9

10		1010		A

11		1011		B

12		1100		C

13		1101		D

14		1110		E

15		1111		F

Another example of binary to hexadecimal conversion:

0010 0100     0011 0101      1000 1100      0001 11112 , is equivalent to

2 4                    3 5                     8 C                     1  F16

Memory:

There are 232 – 1 locations or addresses in memory in which a byte (8 bits) of information can be stored.

The locations can contain data or program instructions (although these are shown as pnemonics below, they are actually stored as numeric values).

Each instruction in MIPS is 32 bits (one word) long.

| Address 1004000016 1001000016 0040000016 0000000016 | Memory Usage in MARS  Heap and Stack (learn more later) |
| --- | --- |
|  |  Data Segment (Data with fixed size) |
|  |  Text Segment (Program Instructions) |
|  |  Reserved |

MIPS instructions for use in Lab today

- Arithmetic (R-type) Instructions

add  $t3,$t1,$t2  # add, $t3 <- contents of $t1 + contents of $t2

addi  $t3, $t1,5   # add immediate,$t3 <- contents of $t1 + 5

- Memory Access Instructions

lw   $t1,label     # load word, $t1 <- value of word stored at					                               memory address/location specified by label

lw  $t1,3($s0)   # load word, $t1 <= value of word stored at

memory address (base address in $s0 + 3)

sw  $t1,label      #  store word, stores value of word in $t1 to						       	address/location in memory  specified by label

(lw and sw can also be byte or halfword, i.e. lb, lh, sb,sh)

- Pseudo-instructions –not part of the basic MIPS instruction set, but used for programmers convenience.  These instructions translate to basic MIPS instructions when the program is assembled (but those basic instructions are not as intuitive from a programmers perspective).

li   $t1, 3 	      # load immediate, $t1 <- 3

la  $s1, label    # load address, $s1 <- address corresponding to label

move $t1,$t2    # move, move contents of $t2 to $t1

Directives – are not instructions, but you use them in your program to tell the assembler how to store your program in memory

.text

.globl main

Precedes your text segment (program instructions), and

specifies main as a global symbol (recognized by other

files in a multi-file project

.data

Precedes your data segment (data declarations)

(text segment can come before data segment, or vice versa)

.ascii  “string”

Defines a string of characters (each character is stored as 				a 1-byte ascii value)

.asciiz “string”

Defines a null-terminated string (ends with a null byte)

.byte b0,b1,b2

Defines and initializes subsequent bytes in memory

.half	h0,h1,h2

Defines and initializes subsequent half-words (16-bit

values – alignment forced to next even address

.word w0,w1,w2

Defines and initializes subsequent words (32-bit values)

– alignment forced to next word address (multiple of 4)

.space n

allocates n bytes of space, usually initialized to 0

SYSCALL functions overview

System services used for input/output

How to use SYSCALL system services

1. Load the service number in register $v0.

2. Load argument values, if any, in $a0, $a1, or $a2

3. Issue the SYSCALL instruction.

4. Retrieve return values, if any, from result registers

Table of Commonly Used Services

| Service | $v0 | Arguments | Result |
| --- | --- | --- | --- |
| print integer | 1 | $a0 = integer to print |  |
| print string | 4 | $a0 = address of null- terminated string to print |  |
| read integer | 5 |  | $v0 contains integer read |
| read string | 8 | $a0=address of input buffer $a1=max. # of chars. to read |  |
| exit (stop execution) | 10 |  |  |
| print character | 11 | $a0=character to print |  |
| read character | 12 |  | $v0 contains character read |
| open file | 13 | $a0=address of null-terminated string containing filename $a1=flags $a2=mode | $v0 contains file descriptor (- if error) |
| read from file | 14 | $a0 = file descriptor $a1=address of output buffer $a2=max. # of chars to read | $v0 contains # of chars. read (0=EOF,- if error) |
| write to file | 15 | $a0 = file descriptor $a1=address of output buffer $a2= # of chars to write | $v0 contains # chars. written (- if error) |
| close file | 16 | $a0 = file descriptor |  |

Examples of Simple I/O for lab today

# print an integer

li $v0,1	# load service number into $v0

li $a0,5	# load value to be printed into $a0

syscall

#print a null-terminated string

li $v0,4 	#load service number in $v0

la $a0,prompt_string

# load address of string to be printed into $a0

syscall         # the null-terminated string must also be defined in the data

segment!



.data

prompt_string:  .asciiz “Enter a value: “

# read in an integer

li $v0,5	#load service number in $v0

syscall	#the value entered by the user is returned in $v0

move $t0,$v0	#store value entered into another register

# read in a string

li $v0,8  		#load service number in $v0

la $a0,answer	#put address of answer string in $a0

lw $a1,alength	#put length of string in $a1

syscall	  	#answer and alength must be defined in data

segment!



.data

answer:  .space 50  # allocate space for string to be stored

alength:  .word 50   #length of string to be entered

# terminate execution of program

#should always be the final instructions executed in program

li $v0,10   #load service number in $v0

syscall